## Slide 1
ENGINEERING VIVA
Implementation of
CORDIC Algorithm
Step-by-Step Calculation of
sin 60° and cos 60°
Student name: [Name] Roll number: [Roll No.]
Department: [Department]
College: [College Name]
x
y
60°
sin 60°
cos 60°
Notes: I will calculate sine and cosine of 60 degrees by rotating a vector in small steps. The first three steps show the arithmetic explicitly, followed by a 16-step table and a comparison with the exact values. This is a numerical explanation of the algorithm, not a claim of measured RTL or FPGA performance.

## Slide 2
SHIFT-AND-ADD TRIGONOMETRY
Introduction to CORDIC
02 / 10
Coordinate Rotation
Digital Computer
Compute sine and cosine using
shifts, additions and subtractions.
FPGA / DSP / Embedded systems
Digital hardware
x
y
60°
Rotated vector
Start on x-axis
Notes: CORDIC stands for Coordinate Rotation Digital Computer. The rotation core uses additions, subtractions and powers-of-two shifts, with precomputed angle constants. Initial scaling compensates for the vector growth. These operations suit FPGA, DSP, embedded and other digital hardware implementations. Point to the rotated vector: its horizontal coordinate gives cosine and vertical coordinate gives sine once gain is compensated. Technical reference: AMD/Xilinx CORDIC v6.0 Product Guide PG105, Functional Description, pages 17–20: https://www.amd.com/content/dam/xilinx/support/documents/ip_documentation/cordic/v6_0/pg105-cordic.pdf. Numerical values are independently calculated from the stated recurrence using full precision, then rounded for display. All displayed angles are degrees.

## Slide 3
SMALL ROTATIONS APPROACH 60°
Basic working principle
03 / 10
αᵢ = atan(2⁻ⁱ), in degrees
xᵢ₊₁ = xᵢ − dᵢ yᵢ 2⁻ⁱ
yᵢ₊₁ = yᵢ + dᵢ xᵢ 2⁻ⁱ
zᵢ₊₁ = zᵢ − dᵢ αᵢ
dᵢ = +1 if zᵢ ≥ 0, otherwise −1
Use the previous x and y in both updates.
Initialize x, y and z
Choose direction from z
Update x, y and z
After 16 steps: read x, y
Repeat until i = 15
Notes: At each step, z is the remaining angle. If z is nonnegative, rotate counterclockwise; otherwise rotate clockwise. The rotation angle is arctan(2^-i), in degrees. The powers of two allow shifts in a fixed-point implementation. Both coordinate updates use the previous x and y. We run exactly 16 iterations, rather than waiting for z to become exactly zero. Technical reference: AMD/Xilinx CORDIC v6.0 Product Guide PG105, Functional Description, pages 17–20: https://www.amd.com/content/dam/xilinx/support/documents/ip_documentation/cordic/v6_0/pg105-cordic.pdf. Numerical values are independently calculated from the stated recurrence using full precision, then rounded for display. All displayed angles are degrees.

## Slide 4
16 ITERATIONS, I = 0 TO 15
Initialize the 60° example
04 / 10
x₀ = K₁₆ ≈ 0.607252935
y₀ = 0
z₀ = 60°
K₁₆ = ∏ᵢ₌₀¹⁵ 1 / √(1 + 2⁻²ⁱ)
K₁₆ compensates for the gain
introduced by the shift-and-add rotations.
i | 2⁻ⁱ | αᵢ (degrees)
0 | 1 | 45.000000°
1 | 0.5 | 26.565051°
2 | 0.25 | 14.036243°
3 | 0.125 | 7.125016°
4 | 0.0625 | 3.576334°
5 | 0.03125 | 1.789911°
Continue the lookup through i = 15.
Notes: The simplified coordinate updates increase length by sqrt(1+2^(-2i)) at each step. I compensate in advance by starting with the reciprocal of the total 16-step gain, K16. Starting at x=1 without compensation would produce scaled outputs. K16 is 0.6072529351031394. The table lists precomputed angles, not trigonometric calculations performed by the rotation hardware. Numerical arithmetic here is unquantized and full precision. Technical reference: AMD/Xilinx CORDIC v6.0 Product Guide PG105, Functional Description, pages 17–20: https://www.amd.com/content/dam/xilinx/support/documents/ip_documentation/cordic/v6_0/pg105-cordic.pdf. Numerical values are independently calculated from the stated recurrence using full precision, then rounded for display. All displayed angles are degrees.

## Slide 5
ITERATION I = 0
Step 1: rotate by +45°
05 / 10
z₀ = +60° d₀ = +1 2⁰ = 1
x₁ ≈ 0.607253 − 0 × 1
≈ 0.607253
y₁ ≈ 0 + 0.607253 × 1
≈ 0.607253
z₁ ≈ 60° − 45° ≈ 15°
Direction: counterclockwise
x
y
45°
60° target
(0.607253, 0.607253)
Notes: Initially z is +60 degrees, so d=+1. At i=0 the shift factor is 1. Since y0=0, x1 remains K. y1 becomes K. The vector now points at 45 degrees and the remaining angle is 15 degrees. The vector length is not yet one: compensation was chosen for all 16 steps. On the next slide, the same axes remain in place to reveal the next rotation.

## Slide 6
ITERATION I = 1
Step 2: overshoot the target
06 / 10
z₁ = +15° d₁ = +1 2⁻¹ = 0.5
x₂ ≈ 0.607253 − 0.607253 × 0.5
≈ 0.303626
y₂ ≈ 0.607253 + 0.607253 × 0.5
≈ 0.910879
z₂ ≈ 15° − 26.565051°
≈ −11.565051°
Negative residual: reverse next.
x
y
71.565°
60° target
(0.303626, 0.910879)
Notes: The remaining angle is still positive, so rotate counterclockwise again. At i=1, multiplying by one half corresponds to a one-bit right shift in fixed-point hardware. The new angle is 45 plus 26.565051, or 71.565051 degrees. The negative residual tells us that the vector passed the target. Displayed operands are rounded for readability; the calculation retains full precision.

## Slide 7
ITERATION I = 2
Step 3: correct with a clockwise turn
07 / 10
z₂ = −11.565051° d₂ = −1
x₃ ≈ 0.303626 + 0.910879 × 0.25
≈ 0.531346
y₃ ≈ 0.910879 − 0.303626 × 0.25
≈ 0.834973
z₃ ≈ −11.565051° + 14.036243°
≈ +2.471192°
The residual is positive again.
x
y
57.529°
60° target
(0.531346, 0.834973)
Notes: The remaining angle is negative, so d=-1 and both coordinate update signs reverse. The factor is one quarter. x increases and y decreases. The angle becomes 57.528808 degrees, slightly below the 60-degree target. Now the residual is positive, so the next rotation is counterclockwise. The algorithm follows the residual sign while the available rotation angles shrink.

## Slide 8
CONVERGENCE TOWARD 60°
The complete 16-step calculation
08 / 10
Updated state after each iteration. Calculations retain full precision.
i | xᵢ₊₁ | yᵢ₊₁ | zᵢ₊₁ (°)
0 | 0.607253 | 0.607253 | 15.000000
1 | 0.303626 | 0.910879 | -11.565051
2 | 0.531346 | 0.834973 | 2.471192
3 | 0.426975 | 0.901391 | -4.653824
4 | 0.483312 | 0.874705 | -1.077490
5 | 0.510646 | 0.859602 | 0.712421
6 | 0.497215 | 0.867581 | -0.182753
7 | 0.503993 | 0.863696 | 0.264861
i | xᵢ₊₁ | yᵢ₊₁ | zᵢ₊₁ (°)
8 | 0.500619 | 0.865665 | 0.041051
9 | 0.498928 | 0.866643 | -0.070855
10 | 0.499775 | 0.866155 | -0.014902
11 | 0.500198 | 0.865911 | 0.013075
12 | 0.499986 | 0.866033 | -0.000914
13 | 0.500092 | 0.865972 | 0.006080
14 | 0.500039 | 0.866003 | 0.002583
15 | 0.500013 | 0.866018 | 0.000835
Final residual: +0.000835°
Notes: Each row gives the updated state after the specified zero-based iteration i. x and y are shown to six decimal places, and the residual z is shown in degrees. All values were calculated without rounding intermediate states. The residual changes sign several times and its absolute value does not decrease at every single step, but the shrinking micro-rotations bring the direction close to the target. Final x16=0.5000126187632938, y16=0.8660181182154755, z16=0.00083485417105244 degrees.

## Slide 9
NUMERICAL RESULT
Final values: read cosine from x, sine from y
09 / 10
cos 60° ≈ 0.500012619
sin 60° ≈ 0.866018118
Function | Reference value | Absolute error
cos 60° | 0.500000000 | 0.000012619
sin 60° | 0.866025404 | 0.000007286
16 iterations with gain compensation.
Fixed-point hardware can change the last digits.
x
y
60°
x ≈ 0.5
y ≈ 0.866
Notes: After 16 iterations, x approximates cosine and y approximates sine. Compare with the exact values cos60=1/2 and sin60=sqrt(3)/2. Absolute error is approximately 1.262e-5 in cosine and 7.286e-6 in sine. The final vector direction is 59.999165145829 degrees. These results use ideal arithmetic, not the quantized Q28 RTL previously supplied. That RTL uses 24 iterations and accepts radians, so it requires degree-to-radian conversion and will have different last digits.

## Slide 10
IMPLEMENTATION SUMMARY
Viva takeaway: one rotation core, two results
10 / 10
Shift by i
Multiply by 2⁻ⁱ
Add or subtract
Follow the sign of z
Read the vector
x gives cos, y gives sin
sin 60° ≈ 0.8660
cos 60° ≈ 0.5000
16 steps. Gain compensated. No general multiplier in the rotation updates.
Notes: The main idea is to replace general trigonometric evaluation with small precomputed rotations. Powers of two become shifts, while additions and subtractions update coordinates. K compensates for gain. Direction depends on the sign of the residual angle. In hardware, the x and y updates must use the same old state. An iterative architecture can reuse one stage, while an unrolled or pipelined architecture uses more hardware. No specific timing or resource result is claimed. Technical reference: AMD/Xilinx CORDIC v6.0 Product Guide PG105, Functional Description, pages 17–20: https://www.amd.com/content/dam/xilinx/support/documents/ip_documentation/cordic/v6_0/pg105-cordic.pdf. Numerical values are independently calculated from the stated recurrence using full precision, then rounded for display. All displayed angles are degrees.